## Slide 1
A Physical-Informed Deep Learning Approach for Event Classification in MATE
Zhiheng Hu
Institute of Modern Physics，CAS
Collaborators:
Hooi Jin Ong
Ningtao Zhang
Zhichao Zhang
Lu Li
Taisen Huang
Enqiang Liu
Institute of Modern Physics,Chinese Academy of Sciences

## Slide 2: Physical motivation and data challenges
Purpose:
Study 11C's nuclear structure and determine whether or not Z=6 proton closed shell exist in 11C by measuring the electric quadrupole transition.
RIBLL1@HIRFL
MATE:
Multi-purpose Active-target Time projection chamber for nuclear astrophysical and exotic beam Experiments
11, 12C : (α, α) , (α, α*)
12C: 75MeV/u, ~105 pps
11C: 55MeV/u, 104-106 pps
Challenges ：
Each experiment generates several TBs data, and how to extract useful information from this massive amount of data becomes a key issue.
The subjectivity and potential biases.
Notes: Therefore, we need to develop a new data processing paradigm—machine learning.
Machine learning is penetrating fundamental nuclear physics research , yielding many successful applications both experimentally and theoretically.

## Slide 3: Convolutional Neural Networks (CNN) for MATE data
Simulation Data with MATESIM toolkit
Simulated Data (64×64)
  15k proton events (12C(p, p)12C)
  15k non-proton events(12C(p, α)9B)
3D track → 2D image
  Charge deposition
  Drift time
MATE Data (simulation) Conversion Flow
z
CNN Work Flow Schematic
Feature Extraction
Classification
CNN general architecture
  Feature Extraction
    input (pre-processing)
    layers
  Classification
FCNN
M.P. Kuchera et al. NIMA(2019)
Notes: In our case, we use the simulation data generated from the MATESIM toolkit. And it comprises two part: 15k proton events (12C(p, p) 12C) and 15k non-proton events(12C(p, α)9B).
The data format generated by the simulation is different from the data format that the model can process. The former is point cloud 3D, and the latter is RGB 2D.
We project the complex 3D track (point cloud) into a 2D information-rich image which represents its charge deposition and drift time.
The information extracted by these layers is also used as the input of FCNN

## Slide 4: Method 1: Benchmark CNN (ResNet-18)
ResNet-18 Architecture
64×64
32×32
16×16
16×16
8×8
4×4
2×2
3 64
64 128
128 256
256 512
1×2
ResNet vs Traditional Architecture
  deeper structure (number of layers)
  enhanced learning capabilities
  effectively capture visual features
Notes: Especially method 3, which can greatly improve the black box nature of machine learning methods and provide interpretability
In contrast to traditional network architecture, ResNet adds an information highway between several convolutional layers. ResNet distinguishes itself by adopting a significantly deeper structure due to it’s special connecting method. It is precisely because of its deeper structure that it has enhanced learning capabilities
We choose the ResNet-18 as our benchmrk due to its great performance.

## Slide 5: Method 1: Benchmark CNN (ResNet-18)
ResNet-18 Architecture
64×64
32×32
16×16
16×16
8×8
4×4
2×2
3 64
64 128
128 256
256 512
1×2
Feature Extraction
Classification
Feature Extraction
Classification
(FCNN)
ResNet vs Traditional Architecture
  deeper structure (number of layers)
  enhanced learning capabilities
  effectively capture visual features
Notes: Especially method 3, which can greatly improve the black box nature of machine learning methods and provide interpretability
In contrast to traditional network architecture, ResNet adds an information highway between each convolutional layer.ResNet distinguishes itself by adopting a significantly deeper structure due to it’s special connecting method. It is precisely because of its deeper structure that it has enhanced learning capabilities
We choose the ResNet-18 as our benchmrk due to its great performance.

## Slide 6: Method 2: Gated-Fusion CNN
MOI Tensor: moment of inertia tensor
(Direction of the trajectory)
Among them, (x, y) repersent the coordinate of picture pixel
Physical knowledge:
Guidance to attach importance to which visual feature channels
: Moment of Inertia about the x-axis
: Moment of Inertia about the y-axis
: Product of Inertia
Feature Extraction
Gating Signal
Classification
(FCNN)
Feature Engineering (MOI Tensor)
Weighted
Gated-Fusion Workflow Schematic
Notes: We introduce physical knowledge to guide the behavior of the model
The core idea of Gated-Fusion is to "let physical knowledge tell the neural network which learned visual feature channels are more worthy of attention."

## Slide 7: Method 3: Cross-Attention CNN
Attention Score Matrix
Context
Vector
Classification
(FCNN)
Query
Vector
Key
Vector
Value
Vector
Cross-Attention
Cross-Attention
Workflow Schematic
Matrix Multiplication
Interpretability of Attention Mechanism
Feature Extraction
Feature Engineering (MOI Tensor)
0.433
0.200
0.113
0.254
Notes: Use physical knowledge to cross-validate the features learned by the model
Compared to Gated Fusion, this approach not only fuses physical information but also inherently provides interpretability.
This interpretability comes from the fact that we can directly see where the model's gaze is.
To gain insight into the decision-making process, we can investigate the attention weights of the last attention layer, just before the final classification."
In terms of specific values, the higher the weight the model assigns to a certain area, the stronger its attention is on the corresponding area.

## Slide 8: Performance Metrics
M.P. Kuchera, R. Ramanujan, J.Z. Taylor et al. Nuclear Inst. and Methods in Physics Research, A 940 (2019) 156–167
TP
#protons
correctly
classified
TN
#non-protons
correctly
classified
FN
#non-protons
incorrectly
classified
FP
#protons
incorrectly
classified
Notes: After the prediction the model made, we can compare the output with true labels of events
A high accuracy indicates model misclassifies is relatively small
A high precision indicates that the model is quite "reliable" and rarely misclassifies good cases as bad ones.
A high recall rate indicates that the model has a "keen eye" and rarely misses the target.
F1 score is a good indicator of the model's overall performance, as it is high only when both precision and recall are high.

## Slide 9: Model Performance Comparison
Model Performance Comparison
Baseline
Gated Fusion
Cross Attention
Performance Metrics

## Slide 10: Summary
CNN is an excellent method for processing three-dimensional tracks, highly suitable for the data analysis process of active target TPCs.
We employed two novel architectures that are currently less applied in nuclear physics, based on simulated datasets of (p,p) and (p,α) reactions, and compared them with traditional methods.
The feasibility of Gated-Fusion and Cross-Attention method have been verified, and they can indeed bring performance improvements to the model.
The next step involves introducing simulated datasets that more closely resemble experimental conditions for further analysis.
Based on the machine learning results, we plan to apply ML methods to the data analysis of MATE.

## Slide 11
Thank You！

## Slide 12: MATE: A new generation detector

## Slide 13: Detailed Motivation
13
Motivation：
The Data Challenge:
A Tsunami of 3D Point-Cloud Data
The Verification Challenge:
The subjectivity and potential biases of a "one-size-fits-all" standard.
Experiments generate massive and complex datasets.Each event is a 3D point-cloud representing the ionization trail of particles.
The sheer volume of data makes manual analysis extremely challenging.
Efficiently and accurately identifying different reaction events is a major bottleneck.
Machine learning methods for track classification in the AT-TPC
Maybe another person’s cutoff

## Slide 14: ResNet-18 detailed Structure
The ResNet-18 network architecture consists of 18 weight layers, including 17 convolutional layers and 1 dense layer.
H. Wu, Y. Wang, Y. Wang et al. Nuclear Inst. and Methods in Physics Research, A 1055 (2023) 168528

## Slide 15: A Further more Motivation ： High-Dimensional Connections
The human brain is good at thinking in two or three dimensions and can only process a limited number of variables at a time.
AI models map positional relationships and concepts into a "latent space" containing hundreds even thousands of dimensions. In this high-dimensional space, two features that appear unrelated to humans may be close together due to some deep, abstract similarities.

## Slide 16: An Automated, Two-Stage Workflow
Stage 1:
The Event Filter
Stage 2:
Detailed Analysis
Raw 3D Event Data (x,y,z,charge)
Input
Project to 2D Dual-Channel Image Charge - 0
Drift Time - 1
Preprocessing
ResNet-18
Binary Classifier
Model
EventLabel
Proton_event or other
Output
Filtered
3D events Filetered by Stage 1
Input
3D Clustering to find individual tracks
DBSCAN/
HDBSCAN
Segmentation
Classify each track via CNN
proton,alpha,etc.
Identification
Predict Physics Parameters Energy,Angle,Vertex
Regression

## Slide 17: N.Further Explanations

## Slide 18: Cross-Attention Performance
Overall Accuracy reached 95.68%, surpassing all previous baselines.
Most critically, the Proton Recall—our primary physics metric—was boosted to 96.67%, a significant improvement over the ResNet-18 baseline's 87.6%.
This demonstrates that our physics-informed architecture is not just more interpretable, but also more effective.
100
Proton：
Overall Accuracy：
proton
non-proton
proton
non-proton

## Slide 19: Attention Entropy
Shannon entropy for a discrete distribution p：
Assume that the attention matrix of a specific head is
Measures the concentration of attention of token i on all tokens
Row Entropy：
Physical Meaning
High entropy: Attention is evenly distributed → Model uncertainty, worth further exploration;
Low entropy: Attention is almost exclusively focused on a single token → Model certainty, but may overfit.

## Slide 20: Attention Entropy
When the model handles different types of misclassified examples, its internal attention mechanism exhibits diametrically opposed "cognitive states":
- For FN examples (missed protons), the model exhibits significant "confusion." Its attention entropy is generally higher and more widely distributed, indicating that when faced with a real proton track, the model is unable to find a clear feature to focus its attention on, resulting in a false negative.
- For FP examples (falsely positive background), the model exhibits high "false confidence." Its attention entropy is generally lower and more concentrated, indicating that the model mistakenly focuses on certain local features (such as a bright cluster of pixels) and makes high-confidence judgments based on this incorrect focus.

## Slide 21: Interpretability Analysis
The model's level of "perplexity" (high attention entropy) shows a strong correlation with the physical form of the track. Specifically, when the model misidentifies a "long" background event as a proton (FP), it exhibits systematic uncertainty.
This reveals a key weakness in the model and provides a clear direction for improvement: the model's ability to discriminate long tracks must be improved, and attention entropy should be used as a reference indicator of decision confidence. When the entropy value is too high, the confidence of the prediction should be reduced.

## Slide 22: Mechanism of Cross-Attention Architecture
Transformer Architecture：
Attention is all you need

## Slide 23: Mechanism of Cross-Attention Architecture
Moment of
Interia Tensor
Parameter Matrix: WQ
Parameter Matrix: WK, WV
Extracted by ResNet-18
Vectors: K & V

## Slide 24: Traditional Workflow
Outlined steps:
1. Clean all events using Hough transform methods.Discard events that have fewer than some preset number of points.
2. Use naive Monto Carlo method to fit every track, assuming that each represents the desired reaction product.
3. Plot a histogram of the objective function for all events.
4.Visually determine a cutoff for a ‘‘good fit’’, or low objective function value.
5.Define all events within that cut as events of interest .
Several Disadvantages:
1. The lack of verfication
2. The subjectivity and potential biases of a "one-size-fits-all" standard.
3. The prejudice raised by preceding steps.
(chain reactions)
These above degrades the efficacy of any ensuing analysis steps.

## Slide 25: Traditional Workflow
Several Disadvantages:
1. The lack of verfication
2. The subjectivity and potential biases of a "one-size-fits-all" standard.
3. The prejudice raised by preceding steps.
Simple Imagery:
Generated by Gemini
amazingly
But we haven't actually heard them singing by ourselves! (corresponding to "independent verification").