## Slide 1
Energy regression
Experiment setup: common image input, two regression routes
1 / 10
180,000 test events (45000 events per track number)
1-4 alpha tracks per event
truth E ~ U[0.3, 4.0] MeV
Five methods compared on the same image:
Cross-Attention and ResNet predict E directly (without reconstructing tracks at all)
RANSAC, Hough, and Hierarchical Clustering reconstruct the track first, then convert range to energy via SRIM.
Objective: To compare the performance of CNNs with that of traditional algorithms(RANSAC, Hough, and Hierarchical Clustering)
⍺ source
E1 = ?
E2 = ?
E3 = ?
E4 = ?
Notes: I will briefly introduce the context and the configuration of the new experiment, Previously, we conducted classification and regression studies using an isotropic alpha source, in which the number of tracks ranges from 1 to 4. After successfully determine the track multiplicity and angles for each event, the next step is to perform energy regression to figure out the ability boundary of each approach further. To this end, we will compare 5 approaches: three traditional algorithms, namely Hough, RANSAC, and Hierarchical Cluster, and two ML approaches, namely Standard ResNet and Cross-Attention ResNet.

## Slide 2
Energy regression
Outline
2 / 10
1. RANSAC Anomaly Investigation and Inference
2. ResNet + Cross Attention Unseen Channel Classification Conclusion
CHANNEL | REACTION | ROLE
A · B | ¹²C(α,p) · ¹²C(α,d) | Trained targets
C · D | ¹²C(α,t) · ¹²C(α,³He) | Trained as “other” (clutter)
null | empty detector | Trained as “other”
E | ¹²C(α,⍺) | Unseen — interpolation probe
F · G · H | ¹³C · ¹⁴C · ¹²C elastic | Unseen — far-OOD carbon probes
3. Next Steps
Notes: I will briefly introduce the context and the configuration of the new experiment, Previously, we conducted classification and regression studies using an isotropic alpha source, in which the number of tracks ranges from 1 to 4. After successfully determine the track multiplicity and angles for each event, the next step is to perform energy regression to figure out the ability boundary of each approach further. To this end, we will compare 5 approaches: three traditional algorithms, namely Hough, RANSAC, and Hierarchical Cluster, and two ML approaches, namely Standard ResNet and Cross-Attention ResNet.

## Slide 3
Energy regression
Anomaly in Conventional Methods
3 / 10

## Slide 4
Energy regression
Identify the Anomaly in Conventional Approach Pipeline
4 / 10
1. Raw Hits — MATEROOT platform
2. Converter — 80×48×2 image (MATE resolution)
3. Fit — track fitting and vertex positioning
4. Reconstructed Range — from fit
5. LISE Projection — range→energy (ext.)
6. Predicted KE — final output
Based on the anomaly classification, visualize the events extracted from the upper band and the shallow band
Notes: This checks whether the gain is only an average effect. The energy-binned plot shows CrossAttention remaining competitive across bins, with the advantage most visible in the low-energy region. The physics caveat is that high-energy tracks are harder because clipping becomes more frequent.

## Slide 5
Energy regression
Anomaly Visualization
5 / 10
Upper band K = 2
Quantity: 1010 (2.24%)
Upper band K = 3
Quantity: 2478 (5.51%)
Upper band K = 4
Quantity: 2694 (5.99%)
Shallow band K = 2
Quantity: 1366 (3.04%)
Shallow band K = 3
Quantity: 1285 (2.86%)
Shallow band K = 4
Quantity: 687 (1.53%)

## Slide 6
Energy regression
Anomaly Analysis
6 / 10
A back-to-back pair is fitted as one track upper band
Fit 1’s corrider occupies Fit 2’s vertex-proximal shallow band
Quantization and Verification

## Slide 7
Energy regression
After Rectification
7 / 10

## Slide 8
Energy regression
Comparison of Hough
8 / 10
This is the anomaly investigation and inference for RANSAC only.
The corresponding investigation for Hough is still in progress.

## Slide 9
Energy regression
Result of Unseen Channel Experiment
9 / 10
CHANNEL | REACTION
A | ¹²C(α,p)
B | ¹²C(α,d)
C | ¹²C(α,t)
D | ¹²C(α,³He)
null | empty detector
E | ¹²C(α,⍺) elastic
F | ¹³C(α,α) elastic
G | ¹⁴C(α,α) elastic
H | ¹²C(12C,12C) elastic
Data-scarce

## Slide 10
Energy regression
Nest Steps
10 / 10
1. Discuss on how to implement Hough with LiLu
2. Manuscript Drafting
3. Discuss on whether it is necessary to add more new work